## Slide 1: Lawful Interception Challenges in Access & Delivery of 3G Networks
Itzik Vager
Telecom Expert
June 2001

## Slide 2: AGENDA
Challenges in LI Access and Delivery for the 3G IP Multimedia Subsystem.
3G LI Challenges in:
  Multi Vendor Networks.
  Mixed GSM and UMTS Networks.
  Pan European Networks
  Shared Infrastructure Networks and Virtual Operators.
  Future Services

## Slide 3: 3rd Generation network layout

## Slide 4: ‘Circuit’ Switched LI - All IP Core
3GPP TS 33.107 Version 4.0.0 Release 4 :
3GPP TS 33.106 Version 5.0.0 Release 5 :
  Multimedia IP Interception Criteria - SIP URL (further study)
  All IP IRI and CC Correlation - For further study
  VHE - Virtual Home Environment - Roaming services will be provided by home network

## Slide 5: 3G Network Internal Multimedia Call

## Slide 6: GPRS based LI Access for IP Multimedia
GPRS Intercepted Session includes a mix of signaling (SIP) and multimedia session transfer.
Session Data (Voice, Video,..) is in compressed format !
Limited information on the activated Multimedia subsystem services (forwarding, conference, etc.)

## Slide 7: 3G Multimedia - Subscriber Identities
Private Identity - NAI
  Used for Registration and AAA.
  May include the IMSI representation.
  Format similar to e-mail address.
  Stored on USIM.
Public User Identity - SIP URL or E.164 Number
  Used for starting a session.
  Multiple Identities, at least one is on USIM.
The home domain name - stored on USIM

## Slide 8: 3G Multimedia call - Roaming scenario

## Slide 9: 3G Multimedia call - Roaming + Conferencing to PSTN scenario

## Slide 10: 3G IP Multimedia - LI Conclusions
LI Access to 3G Multimedia is a must.
Recommended further detailed study by ETSI.
The RELIANT MC will need to face the challenge of handling 3G IP Multimedia sessions, encapsulated in GPRS intercepts.
Upgrading STAR-GATE to interface to VoIP and VoATM will Simplify the interfacing to the 3G Multimedia IP Core.

## Slide 11: STAR-GATE 4 VoIP & VoATM

## Slide 12: 3G Multi Vendor Networks
MVN will be more common.
Network Split based on : 2G/3G, CS/PS, Geographical, Service, Over Time,…
STAR-GATE will provide:
  Flexibility to support different INI protocols.
  Assurance for the integrity of the LI solution.
STAR-GATE

## Slide 13: Mixed GSM / UMTS Networks
Dual Mode mobiles and CN will support continuity of CS and PS calls.
Due to mobility a CS/PS call/session may hand-over between GSM/UMTS CN.
The LI product should be transparent to Inter CN hand-over.
STAR-GATE will interface to 2G / 3G network nodes seamlessly.

## Slide 14: 3G Pan European Networks
The 3G network may span over several countries.
Different countries may have different LI regulation.
Country LI Sovereignty must be maintained.
Operator has local obligation to comply to the local legislation.

## Slide 15: 3G Pan European networks - LI requirements
Provide dedicated, per country, LI Administration.
Provide dedicated, per country LI Delivery variations.
Implement Location based delivery.
Properly handle Ongoing calls/sessions while boarder crossing.

## Slide 16: 3G Pan European networks - The STAR-GATE solution

## Slide 17: 3G Shared Infrastructure Networks and Virtual Operators
Infrastructure Sharing may wear different faces.
LI scenarios need to be studied carefully:
  Target activation in both networks ?
  Roaming between Shared/Non Shared networks.
  Notification of access attempt from the Number Portability Database.
  Providing enough information for Matching of different information sources for the same session.
Partly Share the RN
Virtual Operators
Roaming Agreement
Share RN & SGSNs

## Slide 18: Future services
3G is starving for new money generating services: Gaming, M-Commerce,...
The new services may result in a requirement to upgrade the LI support.
For Example : The use of the Open API to derive the 3G Multimedia IP subsystem.
Other already introduced services - like location based services may catch-up and require integration with LI.

## Slide 19: STAR-GATE and 3G
STAR-GATE is designed for easy upgrade-ability facing the challenges of 3G Networks